## Slide 1
Single Crystal INS data analysis with Horace
Part 1
Notes: 1

## Slide 2
Matlab intro
  Arrays
  Operators
  Indexing
  Objects and methods
Creating sqw file (CLI)
  Powder data
Making cuts
Projections
  Non-orthogonal projections
Sample mis-alignment corrections
  Horace coordinate conventions
Advanced plotting
  Genie-like syntax
  “spaghetti”-plot
Overview

## Slide 3
By default all results are echoed
; operator suppresses output and allows a new statement
  >> no_echo = [1,2; 3,4]; echo = [6,7,8]
... used to continue long commands onto next line
>> gen_sqw (spe, par, sqw, efix, emode, alatt, angdeg,...
u, v, psi, omega, dpsi, gl, gs)
% is the comment operator.
print saves a figure to file
disp displays text on screen
Matlab

## Slide 4
Several types of arrays:
  Numeric arrays (elements are numbers)
  Strings (character arrays)
  Cell arrays (mixed type elements, equivalent to Python list)
1D or 2D can be constructed with the [] or {} operators.
[] used to construct numeric or character arrays
{} used to construct cell arrays
, or space used to delimit elements
; operator used to delimit rows
  >> row_1d = [1,2,3,4]
  >> column_1d = [1;2;3;4]
  >> array_2d = [1,2,3; 4,5,6; 7,8,9]
  >> string = 'abc'
  >> string = ['xyz' num2str(5)] % 'xyz5'
  >> cell_array = {'a', [1,2,3], 'xyz'}
Matlab

## Slide 5
' (dashed / prime) is the transpose operator:
  >> col_vec = [1, 2, 3]'
* denotes matrix-matrix or matrix-vector multiplication
.* is element-wise multiplication
  >> [1,0; 0,1] * [1,2; 3,4] % result: [1,2; 0 0]
  >> [1,0; 0,1] .* [1,2; 3,4] % result: [1,0; 0 0]
  >> [1,0; 0,2] * [1, 1] % error
  >> [1,0; 0,2] * [1; 1] % result: [1; 2]
  >> [1,1] * [1,0; 0,2] % result: [1 2]
  >> [1;1] * [1,0; 0,2] % error
Matlab

## Slide 6
1-based indexing, ranges are inclusive
: operator to indicates ranges
() operator to index into array
step indicated by middle value
arrays are stored column-wise in memory
  >> mm = [1,2,3; 4,5,6; 7,8,9];
  >> mm(1) % ans = 1
  >> mm(1:3,1) % ans = [1, 4, 7]
  >> mm(1:3) % equivalent to mm(1:3,1)
  >> mm(1:2:9) % ans = [1, 7, 5, 3, 9]
N-Dimension arrays indexed by n-arguments – e.g. mm(1,2,3,4)
Matlab

## Slide 7
Blocks need explicit end keyword.
for loops requires a row vector as input
== is equality, || is “or” operator, && is “and” operator
  >> for i = [1,2,3,4]; disp(i); end % Prints 1,2,3,4
  >> j=0; for i = 1:10; j = j + i; end; j % j = 55
  >> if 1 == 2; disp('something weird'); end % Prints nothing
“dot notation” is used to access object properties or methods
Class methods can also be called using the method name with the object as the first argument:
  object.property
  object.method(x,y,z)
  method(object, x, y, z)
Matlab
Just an example (syntax will not work – no object called “object”)

## Slide 8
Don’t need to memorise previous
Access this presentation at:
https://github.com/pace-neutrons/edatc/blob/main/presentations/edatc21_slides_03_horace1.pptx

## Slide 9
Matlab intro
  Arrays
  Operators
  Indexing
  Objects and methods
Creating sqw file (CLI)
  Powder data
Making cuts
Projections
  Non-orthogonal projections
Sample mis-alignment corrections
  Horace coordinate conventions
Advanced plotting
  Genie-like syntax
  “spaghetti”-plot
Overview

## Slide 10
Horace is mainly a command-line interface (CLI) program
Today, we’ll introduce this CLI.
Recap – basic tasks using Horace:
  Creating a 4D S(Q,ω) dataset (sqw file) from runs at different angles
  Viewing / plotting this data in particular (Q,ω) regions
  Fitting the data
https://pace-neutrons.github.io/horace-docs/3.5.0/
>> help <command> % e.g. help gen_sqw
Horace
← gen_sqw
← cut_sqw
← multifit

## Slide 11
gen_sqw (spe_files, par_file, sqw_file, efix, emode, alatt, angdeg, u, v, psi, omega, dpsi, gl, gs)
spe_files – cell array (list) of reduced data file names
par_file – detector parameter file (not usually used)
sqw_file – output sqw file name
efix – fixed energy (Ei for direct geometry)
emode – 1 for direct, 2 for indirect
alatt – [a,b,c] lattice parameters
angdeg – [alpha,beta,gamma] lattice angles (in degrees)
u, v – vectors defining the horizontal scattering plane
psi – a vector of rotation angles about the vertical axis (in degrees)
omega, dpsi, gl, gs – sample misalignment angles (in degrees)
gen_sqw
n
u
v
ψ
Ω
GL
GS

## Slide 12
gen_sqw_powder(spe_files, par_file, sqw_file, efix, emode)
spe_files – cell array (list) of reduced data file names
par_file – detector parameter file (not usually used)
sqw_file – output sqw file name
efix – fixed energy (Ei for direct geometry)
emode – 1 for direct, 2 for indirect
alatt – [a,b,c] lattice parameters
angdeg – [alpha,beta,gamma] lattice angles (in degrees)
u, v – vectors defining the horizontal scattering plane
psi – a vector of rotation angles about the vertical axis (in degrees)
omega, dpsi, gl, gs – sample misalignment angles (in degrees)
gen_sqw_powder

## Slide 13
w = cut_sqw(data_source, proj, p1_bin, p2_bin, p3_bin, p4_bin)
>> help sqw/cut
data_source – a filename (string) or a sqw object in memory
proj – a projection object (more details next)
p1_bin, p2_bin, p3_bin – vector defining binning along u1, u2, u3
p4_bin – vector defining binning along energy axis
u1, u2, u3 are defined by the projection proj.
Bins can be either 1, 2, or 3 numbers:
  [bin_size] – 1 number rebin full limit of data in this axis with new bin_size
  [lo, hi] – integrate over this axis between lo and hi limits.
  [lo, bin_size, hi] – rebin this axis between lo and hi limits with new bin_size
cut_sqw

## Slide 14
Recap – 2 types of coordinates systems used by Horace:
  u and v vectors defining the horizontal plane in generating the data
  u, v (and optional w) vectors defining Q-axes for cuts
A projection is used to define 3 vectors u1, u2, u3 which define the 3 Q axes for cuts/plots.
A projection is a class with properties:
  u – the first axis
  v – the second axis
  w – the third axis
  type – a string of 3 letters: ‘r’=r.l.u., ‘a’=absolute (Å-1)
  nonorthogonal – true or false (default: false)
nonorthogonal=true means u1=u, u2=v, u3=w
nonorthogonal=false means u1=u; u2 ⊥ u1 in plane of u,v; u3 ⊥ u,v
Horace projections
← “projection”

## Slide 15
Matlab graphs can only have orthogonal plot axes.
  Using nonorthogonal=true gives a distorted view
Nonorthogonal projections
nonorthogonal=false
nonorthogonal=true

## Slide 16
Current version of Horace can only handle 3D rectilinear projections.
Work currently in progress to allow definition of projections defined by a general transformation of Q.
This will include:
  Powder projection
  Cylindrical projection
Generic projections

## Slide 17
w = cut_sqw(data_source, proj, p1_bin, p2_bin, p3_bin, p4_bin)
w = cut_sqw(data_source, proj, p1_bin, p2_bin, p3_bin, p4_bin, '-nopix')
Recap: Horace can create two types of objects using cut:
  dnd (d1d, d2d, d3d, d4d)objects contain only histogrammed (binned) data
  sqw objects contains both histogrammed data which can be plotted and all the detector-energy elements (“pixels”) which were rebinned.
dnd objects are created with the '-nopix' flag – good for plotting as don’t take up much memory
sqw objects (created by default) needed for a lot of operations (re-rebin, symmetrisation, resolution convolution)
smooth only works on dnd.
cut_sqw

## Slide 18
cut_sqw
w1 = cut_sqw('iron_powder.sqw', 0.05, 5, '-nopix')
proj = projaxes([1,1,0], [-1,1,0], 'type', 'rrr');
w1 = cut_sqw('iron.sqw', proj, [-2,0.05,3],[-1.1,0.9],[-.1,.1], 5, '-nopix')
4D sqw file
2D sqw file

## Slide 19
Questions so far?

## Slide 20
Matlab intro
  Arrays
  Operators
  Indexing
  Objects and methods
Creating sqw file (CLI)
  Powder data
Making cuts
Projections
  Non-orthogonal projections
Sample mis-alignment corrections
  Horace coordinate conventions
Advanced plotting
  Genie-like syntax
  “spaghetti”-plot
Overview

## Slide 21
https://pace-neutrons.github.io/horace-docs/3.5.0/Correcting_for_sample_misalignment.html
bragg_positions() – make cuts and fit Bragg peaks automatically
bragg_positions_view() – function to view Bragg peak fits
refine_crystal() – function to calculate a transformation matrix to convert from original (hkl) to corrected (hkl) from the Bragg position fits
change_crystal() – applies the correction matrix to data in memory
change_crystal_horace() – applies correction matrix to sqw file
crystal_pars_correct() – calculate “correct” lattice parameters / angles and misalignment orientation (dpsi, gl, gs) from correction matrix
uv_correct() – calculate u and v vectors defining the true horizontal plane.
Sample misalignment corrections

## Slide 22
https://pace-neutrons.github.io/horace-docs/3.5.0/Plotting.html
Horace 1D and 2D plots are not quite standard Matlab plots and use their own syntax based on the (now defunct) “Genie” program
plot(object) – object can be sqw or dnd. Replaces current plot if it exists
acolor, aline, amark – alter default color, line, marker (applies to next plot)
lx, ly, lz – sets limits in x, y, z directions (z=color axis in 2D)
keep_figure – next plot command will create a new figure window.
make_current – next plot command will replace current plot in figure window.
pl, pm, pe, pp – 1D, overplots line, markers, errors or points (markers+errors)
pd, ph – 1D only, overplots data (markers+errors+line) or histogram
ds – 2D, plots a contour map of the data
Advanced Plotting

## Slide 23
pl, pm, pe, pp – 1D, overplots line, markers, errors or points (markers+errors)
pd, ph – 1D only, overplots data (markers+errors+line) or histogram
Advanced Plotting

## Slide 24
ds – 2D, plots a contour map of the data
Advanced Plotting

## Slide 25
spaghetti_plot – function to plot data along particular Q directions
spaghetti_plot([0,0,-3; 0,0,-3.5; -0.5,0,-3.5; -0.5,0,-3; -2/3 1/3 -3; 0 0 -3], 'upd3_ei25.sqw', 'labels',{'\Gamma','A','L','M','K','\Gamma'}, 'ebin',[3,0.2,20], 'qbin',0.025, 'qwidth',0.1)
Advanced Plotting

## Slide 26
Questions so far?
(and 5 min break)

## Slide 27
Horace CLI Demonstration
Horace CLI Demonstration

## Slide 28
help <command>
https://pace-neutrons.github.io/horace-docs/3.5.0
gen_sqw – needs u, v vectors to define the horizontal scattering plane
cut_sqw – needs another set of u,v,w to define cut axes (called projections).
gen_sqw_powder – note has only 2 axes.
Horace plots use a “Genie” syntax (see docs) rather than standard Matlab syntax.
Summary