## Slide 1
Single Crystal INS data analysis with Horace
Part 3
Notes: 1

## Slide 2
Overview
Yesterday
  Intensity corrections
  Background subtraction
  Symmetrisation
  Data diagnostics
    Identifying spurions
    Masking data
  Simulating data
Today
  Fitting
  Resolution convolution

## Slide 3
Recap
3 ways of creating a synthetic workspace in Horace:
  func_eval(w_in, @fun, par)
  sqw_eval(w_in, @sqwfun, par)
  disp2sqw_eval(w_in, @dispfun, par, fwhm)
  function out = fun(x, y, par)
  xc = par(1); yc = par(2); sigx = par(3); sigy = par(4);
  out = par(5) * exp(-(x-xc).^2./(2*sigx)-(y-yc).^2./(2*sigy));
  end

## Slide 4
Recap
3 ways of creating a synthetic workspace in Horace:
  func_eval(w_in, @fun, par)
  sqw_eval(w_in, @sqwfun, par)
  disp2sqw_eval(w_in, @dispfun, par, fwhm)
  function out = sqwfun(h,k,l,en,par)
  JS = par(1); Gam = par(2);
  omega = JS * (1-cos(pi*h));
  out = par(3) * Gam ./ ((en - omega).^2 + Gam.^2);
  end

## Slide 5
Recap
3 ways of creating a synthetic workspace in Horace:
  func_eval(w_in, @fun, par)
  sqw_eval(w_in, @sqwfun, par)
  disp2sqw_eval(w_in, @dispfun, par, fwhm)
3 different function signatures depending on the evaluation mechanism
These three types of functions can also be used for fitting
  func_eval → multifit
  sqw_eval → multifit_sqw
  disp2sqw_eval → multifit_sqw and disp2sqw
  function [w,s] = dispfun(h,k,l,par)
  w = par(1) * (1-sin(pi*h));
  s = par(2) + w*0;
  end

## Slide 6
multifit
multifit is the Horace fitting class.
  https://pace-neutrons.github.io/horace-docs/3.5.0/Multifit.html
  Uses the Levenberg-Marquardt algorithm
  Designed to fit multiple cuts simultaneously
  Expects user-defined model functions in the form func(x1,x2,x3,…,pars)
  Can also have non-Matlab fit functions (e.g. Fortran, C/C++, Python)
    Beta: work-in-progress contact me for details
Accepts up to two model functions: “foreground” and “background”.
Has the concept of a “local” and “global” model functions:
  “global”: parameters are the same for all input cuts
    By default “foreground” model function is “global”
  “local”: parameters for each cut is different
    By default “background” model function is “local”
Can specify “bindings” (or “ties”) between model/background parameters
  https://pace-neutrons.github.io/horace-docs/3.5.0/Multifit.html#binding-parameters

## Slide 7
multifit
multifit has two types of syntax
“legacy” function-style syntax:
  >> [w_fit, fitpars] = multifit(w_in, @fun, init_par)
Object oriented syntax:
  >> mfobj = multifit(w_in)
  >> mfobj = mfobj.set_fun(@fun)
  >> mfobj = mfobj.set_pin(init_par)
  >> [w_fit, fitpars] = mfobj.fit()
Object-oriented syntax is highly recommended for complex multi-cut fits with background and bindings between model/background parameters.

## Slide 8
Make a 1D cut and fit a set of Gaussians to it.
  >> w1 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), 0.05, [-1.1,-0.9], [-0.1, 0.1], [100,120])
  >> [wf, fp] = multifit(w1, @mgauss, [0.4 -0.8 0.1 0.4 -0.2 0.1 0.4 0.2 0.1])
  >> plot(w1); pl(wf)
A simple fit

## Slide 9
Make a 1D cut and fit a set of Gaussians to it.
  >> w1 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), 0.05, [-1.1,-0.9], [-0.1, 0.1], [100,120])
  >> [wf, fp] = multifit(w1-0.2, @mgauss, [0.4 -0.8 0.1 0.4 -0.2 0.1 0.4 0.2 0.1])
  >> plot(w1-0.2); pl(wf)
A simple fit

## Slide 10
Make a 1D cut and fit a set of Gaussians to it.
  >> w1 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), 0.05, [-1.1,-0.9], [-0.1, 0.1], [100,120])
  >> [wf, fp] = multifit(w1, @mgauss, [0.4 -0.8 0.1 0.4 -0.2 0.1 0.4 0.2 0.1], @linear_bg, [0.2 0])
  >> plot(w1); pl(wf)
A simple fit

## Slide 11
Make a 1D cut and fit a set of Gaussians to it.
  >> w1 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), 0.05, [-1.1,-0.9], [-0.1, 0.1], [100,120])
  >> mf = multifit(w1); mf = mf.set_fun(@mgauss); mf = mf.set_pin([0.4 -0.8 0.1 0.4 -0.2 0.1 0.4 0.2 0.1]);
  >> mf = mf.set_bfun(@linear_bg); mf = mf.set_bpin([0.2 0]);
  >> [wf, fp] = mf.fit(); plot(w1); pl(wf)
A simple fit
Object-oriented syntax

## Slide 12
Now try to fit the same dataset with a S(Q,E) model
  >> w1 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), 0.05, [-1.1,-0.9], [-0.1, 0.1], [100,120])
  >> [wf, fp] = multifit_sqw(w1, @my_disp, [200, 0.4, 0.1])
  >> plot(w1); pl(wf)
S(Q,E) model fit
function out = my_disp (qh, qk, ql, en, par)
om = par(1)*abs(cos(pi*qh));
out = par(2)*exp(-((om-en).^2)./(2*par(3)));
end
my_disp.m

## Slide 13
Now try to fit the same dataset with a S(Q,E) model
  >> w1 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), 0.05, [-1.1,-0.9], [-0.1, 0.1], [100,120])
  >> ff_fun = MagneticIons('Fe0').getFF_calculator(w1);
  >> [wf, fp] = multifit_sqw(w1, @my_disp_ff, {[200, 0.4, 0.1] ff_fun})
  >> plot(w1); pl(wf)
S(Q,E) model fit
function out = my_disp (qh, qk, ql, en, par, ff_fun)
om = par(1)*abs(cos(pi*qh));
out = par(2)*exp(-((om-en).^2)./(2*par(3)));
out = out .* ff_fun(qh,qk,ql,en)';
end
my_disp_ff.m

## Slide 14
Now try to fit the same dataset with a S(Q,E) model
  >> w1 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), 0.05, [-1.1,-0.9], [-0.1, 0.1], [100,120])
  >> ff_fun = MagneticIons('Fe0').getFF_calculator(w1);
  >> [wf, fp] = multifit_sqw(w1, @my_disp_ff, {[200, 0.4, 0.1] ff_fun}, @linear_bg, [0.1, 0])
  >> plot(w1); pl(wf)
S(Q,E) model fit
function out = my_disp (qh, qk, ql, en, par, ff_fun)
om = par(1)*abs(cos(pi*qh));
out = par(2)*exp(-((om-en).^2)./(2*par(3)));
out = out .* ff_fun(qh,qk,ql,en)';
end
my_disp_ff.m

## Slide 15
Now try to fit the S(Q,E) model to a 2D dataset
  >> w2 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), [-3,0.05,3], [-1.1,-0.9], [-0.1, 0.1], [50,5,300])
  >> ff_fun = MagneticIons('Fe0').getFF_calculator(w2);
  >> wf2 = multifit_sqw(w2, @my_disp_ff, {[200, 0.4, 0.1] ff_fun});
  >> plot(w2); keep_figure; plot(wf2)
S(Q,E) model fit

## Slide 16
What about evaluating the 1D fit parameters of the S(Q,E) model in 2D?
  >> w1 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), 0.05, [-1.1,-0.9], [-0.1, 0.1], [100,120])
  >> w2 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), [-3,0.05,3], [-1.1,-0.9], [-0.1, 0.1], [50,5,300])
  >> ff_fun = MagneticIons('Fe0').getFF_calculator(w2);
  >> [wf, fp] = multifit_sqw(w1, @my_disp_ff, {[200, 0.4, 0.1] ff_fun})
  >> wf2 = sqw_eval(w2, @my_disp_ff, {fp.p ff_fun});
  >> plot(w2); keep_figure; plot(wf2)
S(Q,E) model fit
Dispersion model is incorrect!

## Slide 17
Now try to fit the S(Q,E) model to an array of 1D dataset
  >> proj = projaxes([1,1,0], [-1,1,0], 'type', 'rrr');
  >> en=80:20:160; for i = 1:numel(en); wc(i) = cut_sqw('iron.sqw', proj, 0.05, [-1.1,-0.9], [-0.1, 0.1], [-10 10]+en(i)); end
  >> ff_fun = MagneticIons('Fe0').getFF_calculator(wc(1));
  >> [wf, fp] = multifit_sqw(wc, @my_disp_ff, {[200, 0.4, 0.1] ff_fun}, @linear_bg, [0.1, 0])
  >> for i = 1:numel(en); plot(wc(i)); pl(wf(i)); ly(0,1); keep_figure; end
S(Q,E) model fit

## Slide 18
Evaluating the 1D fitted parameters on the 2D plot?
  >> proj = projaxes([1,1,0], [-1,1,0], 'type', 'rrr');
  >> en=80:20:160; for i = 1:numel(en); wc(i) = cut_sqw('iron.sqw', proj, 0.05, [-1.1,-0.9], [-0.1, 0.1], [-10 10]+en(i)); end
  >> ff_fun = MagneticIons('Fe0').getFF_calculator(wc(1));
  >> [wf, fp] = multifit_sqw(wc, @my_disp_ff, {[200, 0.4, 0.1] ff_fun}, @linear_bg, [0.1, 0])
  >> wf2 = sqw_eval(w2, @my_disp_ff, {fp.p ff_fun});
  >> plot(w2); keep_figure; plot(wf2)
S(Q,E) model fit

## Slide 19
Use multifit for functions which needs the plot axes (defined by the projection) – e.g. peak or linear functions
  These functions are dimension specific (e.g. need different functions for 1D, 2D, 3D datasets)
User multifit_sqw for functions which needs the (h,k,l,en) coordinates – e.g. dispersion models
Can fit multiple cuts simultaneously
Can fit (sum of) two model functions (“foreground” and “background”) together.
By default, foreground functions have “global” parameters (same for all cuts), and background functions have “local” parameters (different for each cut)
Fitting summary

## Slide 20
Questions so far?

## Slide 21
Resolution Convolution
The measured intensity at the detector is:
has contributions from:
  Moderator time width
  View aperture size / guide divergence
  Chopper opening time width
  Sample size
  Detector size / detector width (time)
Often the resolution function is approximated as Gaussian
  The asymmetry of the moderator pulse means this is not valid for ToF spectrometers
  But Horace can still calculate a 4D Gaussian for you if you want…
In Horace, the convolution (integration) is computed numerically using the Monte Carlo method.
most
important
least
(for ToF direct
spectrometers)

## Slide 22
Resolution Convolution Details
The contributions to the resolution function can be expressed in 11 variables:
  tm – time deviation at the moderator
  ya, za (or γy, γz) – the coordinates of the neutron at the aperture (or neutron guide divergences)
    TobyFit was designed when neutron guides did not exist. Guide divergence broadening is approximated by a large aperture (beam-port window)
  tch – time deviation at the chopper
  xs, ys, zs – neutron coordinate at the sample
  xd, yd, zd, td – neutron coordinate at the detector
These 11 deviations from the ideal case (bin centre or pixel coordinate) are sampled randomly producing a vector Y
The distributions from which Y is sampled depends on the sample and instrument
There is a linear transformation which maps Y to the sample frame coordinates (Q,E)
(δQ, δE) = T B Y
where the T and B matrices are given in Toby’s thesis, Appendix A (eq. A.66 and Table A1 respectively)
The (Q+δQ, E+δE) vector is then passed to the sqw model function.
T. G. Perring, High Energy Magnetic Excitations in Hexagonal Cobalt, Ph.D. Thesis, University of Cambridge, 1991
RAL Technical Report RALT-028-94

## Slide 23
So:
Is transformed into:
where (Q0,E0) is the coordinate of each pixel – that is I(Q0,E0) is the calculated intensity of each pixel
By default N=10 (mc_points) is used because there are a lot of pixels and they overlap significantly.
But this means that it takes 10x longer for the resolution calculation than without…
Resolution Convolution

## Slide 24
Resolution Convolution
Use the tobyfit class to calculate or fit with resolution convolution
First need to define a sample (IX_sample) and instrument on the workspace to be fitted or simulated.
  >> w1 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), 0.05, [-1.1,-0.9], [-0.1, 0.1], [100,120]);
  >> xdir = [1,0,0]; ydir = [0,1,0]; ei = 401; freq = 600; chop_type = 's';
  >> w1 = set_sample(w1, IX_sample(xdir, ydir, 'cuboid', [0.03,0.03,0.03]));
  >> w1 = set_instrument(w1, maps_instrument(ei, freq, chop_type));
  >> ff_fun = MagneticIons('Fe0').getFF_calculator(w1);
  >> tf = tobyfit(w1);
  >> tf = tf.set_fun(@fe_sqw_ff);
  >> tf = tf.set_pin({[200 200 0.1] ff_fun});
  >> tf = tf.set_bfun(@linear_bg);
  >> tf = tf.set_bpin([0.1 0]);
  >> wsim = tf.simulate()
  >> plot(w1); pl(wsim)
Need to use object oriented interface
but otherwise exact same syntax as for
multifit

## Slide 25
Finally, can use the resolution_plot function to plot a resolution ellipsoid on a 2D cut (only 2D cuts).
  >> w1 = cut_sqw('iron.sqw', projaxes([1,1,0], [-1,1,0], 'type', 'rrr'), [0.5,0.05,1.5], [-1.1,-0.9], [-0.1, 0.1], [50,5,150]);
  >> xdir = [1,0,0]; ydir = [0,1,0]; ei = 401; freq = 600; chop_type = 's';
  >> w1 = set_sample(w1, IX_sample(xdir, ydir, 'cuboid', [0.03,0.03,0.03]));
  >> w1 = set_instrument(w1, maps_instrument(ei, freq, chop_type));
  >> cov = resolution_plot(w1)
Resolution Convolution
cov is the covariance matrix
This uses the Gaussian approximation

## Slide 26
Questions so far?
(and 5 min break)

## Slide 27
Horace CLI Demonstration
Horace CLI Demonstration

## Slide 28
Two types of fitting in Horace:
  (simpler) Functions of the plot (projection) axes coordinates
    func_eval, multifit
    function out = model(x1, x2, …, xn par)
    Need to define different functions for different N-dimensions
  S(Q,E) model functions
    sqw_eval, multifit_sqw
    function out = model(qh, qk, ql, en, par)
    Can work for any dimensional objects
Need to use the tobyfit class to simulate or fit with resolution convolution.
Define the sample and instrument on the cut first
tobyfit uses exact same syntax as multifit
Summary